## Slide 1
Spatial Models – Raster
Stacy Bogan
sbogan@cga.harvard.edu

## Slide 2: Raster data are made of pixels
Surface of values composed of square
pixels each with a specific value
10 m
Pixels are a specific
size (ex. 10 m)
3
10 m
Pixels are arranged in rows and columns

## Slide 3: Pixel Size = Spatial Resolution

## Slide 4: Pixel Size Matters!

## Slide 5: Advantages of Raster Data
Represents a data surface. Every location within the raster extents has a value
Sometimes smaller file size than shapefiles containing the same amount of data
Looks good on a map if you’re not close to the raster resolution

## Slide 6
Disadvantages of Raster Data
Doesn’t look so good on a map if you try to zoom in close to the raster resolution
Coarse resolution raster data don’t translate well to finer resolutions

## Slide 7: Types of Raster Data
Continuous
Floating point or Integer
Examples: Topography, satellite imagery, distance grids

## Slide 8: Types of Raster Data
Discrete or Thematic
Could be binary (1,0)
Could be limited number of unique values
Examples: Land cover classification, true/false suitability

## Slide 9
You can always Reclassify
Continuous to Discrete,
but never Discrete to Continuous

## Slide 10: Some Popular Raster Formats
ESRI Grid
Geo TIFF
IMG
JPEG
MrSID
netCDF
HDF
USGS DEM

## Slide 11: Raster Attribute Tables
Discrete raster data can have an attribute table
OID, VALUE, & COUNT fields can not be changed
You can add fields, calculate fields, & join tables just like with vector data

## Slide 12: Rendering and Symbolizing
Stretched – continuous data displayed across a gradual ramp of colors
RGB Composite – multi-band data in three filters

## Slide 13: Rendering and Symbolizing
Classified – displays thematic rasters by grouping cell values into classes
For example, classifying a range of soil types into “suitable” to “not suitable” for vineyards

## Slide 14: Raster Processing Tools in ArcGIS
Create rasters from vectors with Spatial Analyst Tools
  Interpolation
  Density
  Distance
  Polygon to Raster (Data Management Tools)

## Slide 15: Raster Processing Tools in ArcGIS
Collect raster data with vectors
  Zonal statistics
  Extract values to points
Raster Calculator for Overlay
  Simple Arithmetic
  Algebra
  Geometry

## Slide 16: Raster Processing Tools in ArcGIS
For example, create a new grid of elevation greater than 600 m

## Slide 17: Terrain Analysis
Slope - degree or percent
Aspect - slope direction (0- 360˚)
Viewshed – which cells are visible from point locations
Catchment – e.g. watersheds
Flow path - distance of water flow to point

## Slide 18: Hillshade for Texture Visualization

## Slide 19: Distance Calculation

## Slide 20: Gypsy Moth Risk in Michigan
Using overlays to identify stands of forest that are at high risk of gypsy moth infestation.

## Slide 21: Land Use / Land Cover Change

## Slide 22: Land Use / Land Cover Change
Which land covers gained and lost between the time period?
Which land covers gained or lost to which others?

## Slide 23: Multi-Criterion Evaluation (MCE)
Combining multiple pieces of information to address a research question.
Variables are put into a similar scale, and can be weighted for importance.
Raster math is used to create the final output.
Farmland risk index for fracking development in Southwestern Pennsylvania