## Slide 1: Planning a Remote Sensing Project
Stacy Bogan 2/13/2018
Advanced Remote Sensing
Land Use / Land Cover Change Analysis
Module 1

## Slide 2: Module Outline
Planning for a land use / land cover change analysis remote sensing project
  Collect background information
  Select a classification scheme
  Select a remotely-sensed dataset
  Build a scene model

## Slide 3: Collect Background Information
What is the phenomenon you want to study?
What reflectance would you expect in the different areas of the electromagnetic spectrum?
What are the other land covers that you need to differentiate?
What are the physiological processes dictating the spectral reflectance patterns?
Are there different patterns during different times of the year?

## Slide 4: Select a classification scheme
Different schemes require different types of input information
One good web-based tool for choosing which bands to use is the USGS Spectral Characteristics viewer: http://landsat.usgs.gov/tools_spectralViewer.php

## Slide 5: USGS Spectral Library
http://speclab.cr.usgs.gov/spectral.lib06/

## Slide 6: ASTER Spectral library
http://speclib.jpl.nasa.gov/

## Slide 7: Collect Spectra in the field

## Slide 8: Develop training sites

## Slide 9: Select possible datasets
Name | Launched | Pixel size | Swath | Temporal | Spectral
NOAA/AVHRR | 1978 | 1 Km | 2600 km | daily | 4 - 6 bands
Landsat | 1970 | 30 m | 183 km | 16 days | 7 bands
SPOT | 1998 | 20 m | 60 Km | 2-3 days | 4 - 6 bands
ASTER | 2000 | 15 - 30 m | 60 Km | 16 days | 14 bands
MODIS | 2001 | 250m - 1 Km | 2300 Km | 2-3 days | 36 bands

## Slide 10: example Scene model: Burn Monitoring in San Diego County, CA
Environment Type | Forest and shrub
 | Mediterranean Type Ecosystem
Spatial Scale | grain = smallest burned vegetation 1m - 5m
 | extent = San Diego County 144 x 102 km
Temporal Scale | One image per week during May - October
Spatial dimensions | H resolution
 | grain: 1m - 5m
 | extent: 144 km x 102 km
Temporal dimensions | May - October
Spectral dimensions | blue (400-500 nm)
 | green (500-600 nm)
 | red (600-680 nm)
 | NIR (750-900 nm)
Radiometric dimensions | 11 bit
Error tolerance levels | error < smallest unit of measurement, 1-5m

## Slide 11: Data Compliance Matrix
Parameter | Scene Model | Data, IKONOS | Level of Match | Data, 4 bands of LANDSAT TM | Level of Match
Spatial |  |  |  |  | 
pixel size | 1-5m | 4m | suitable | 30m | unsuitable
scene extent | 144 x 102 km | 11 x 11 km | suitable | 185 km x 185 km | suitable
H/L resolution | H | H | suitable | L | unsuitable
Spectral |  |  |  |  | 
No. of Bands | 4 | 4 | suitable | 4 | suitable
Position of Bands | blue | blue |  | blue | 
 | green | green |  | green | 
 | red | red |  | red | 
 | NIR | NIR |  | NIR | 
Radiometric |  |  |  |  | 
resolution | 10 bit | 11 bit | suitable | 8 bit | unsuitable
Temporal |  |  |  |  | 
Date | May - October | yearly | suitable | yearly | suitable
Scale | 1 per week | every 3 days | suitable | every 16 days | suitable
Time + Cost | imagery | high* | depends on | free | suitable
 | processing | high** | budget | moderate | suitable

## Slide 12: Want to learn more? Related Modules
Module 2:
How to download Landsat Data
Module 3:
Processing Level1 Landsat Data
  Atmospheric Correction
Module 4:
Analysis with the Land Change Modeler

## Slide 13: Thank you! Please submit feedback http://gis.harvard.edu/form/workshop-evaluation-form