## Slide 1: Atmospheric Correction
Stacy Bogan 2/13/2018
Advanced Remote Sensing
Land Use / Land Cover Change Analysis
Module 3

## Slide 2: Module Outline
Atmospheric Correction on Level1 Landsat Data
  Collecting data needed for TerrSet AtmosC module
  Running correction
  https://clarklabs.org/tutorial-videos/

## Slide 3: Scene in Pará, Brazil

## Slide 4: Scene in Pará, Brazil
Before Correction
After Correction
Landsat 5 TM data Collected July 12, 2009 at 1:37 pm

## Slide 5: TerrSet ATMOSC Module COS(t) Model
Band | Year | Month | Day | TimeStamp | GMT | Wavelength of Band Center | DN Haze/ RAD Haze | offset | gain | Dn max | Viewing Angle | Sun elevation
1 | 2009 | 7 | 12 | 13:37:01 | 13.61694 | 0.485 | 3.042 | 0 | 1 | 1023 | 0 | 50.41912
2 | 2009 | 7 | 12 | 13:37:01 | 13.61694 | 0.56 | 1.952 | 0 | 1 | 1023 | 0 | 50.41912
3 | 2009 | 7 | 12 | 13:37:01 | 13.61694 | 0.66 | 0.9276 | 0 | 1 | 1023 | 0 | 50.41912
Collect sun elevation and timestamp from metadata
Convert timestamp to decimal
Collect haze value from each band image

## Slide 6: IDRISI ATMOSC Module COS(t) Model
Find the haze value over a deep, clear body of water with the Inquire tool

## Slide 7: Want to learn more? Related Modules
Module 1:
Planning a Remote Sensing Project
Module 2:
Downloading Landsat Data
Module 4:
Analysis with the Land Change Modeler
https://clarklabs.org/tutorial-videos/

## Slide 8: Thank you! Please submit feedback http://gis.harvard.edu/form/workshop-evaluation-form